## Slide 1: Explicit Parallel Call (XPC) Architecture Overview
Ji Kim
BRG Group Meeting 09/19/14
1/21
Notes: (Potentially explain taxonomy of irregularity of applications) (Tao, irregularity paper)
Cut some uninteresting applications (redundant?)
Cornell faculty member mention
This is an experience paper: findings from parallelizing some apps, share with community
  Leveraging old techniques in context of morph algorithms

## Slide 2: Motivation
Age of ILP -> DLP/TLP -> specialization
Trend toward heterogeneous architectures (Intel Haswell, AMD Kabini, NVIDIA Tegra, etc.)
Motivation Data Parallelism XPC Hardware XPC Software Adaptive Acceleration
2/21
Notes: Before year 2000, chip design focused on exploiting ILP with complex, monolithic designs increasing single-threaded performance
However, at some point, this approach was not enough to make the best use of increasing transistor density, especially with emerging constraints like energy efficiency
For the next decade, the focus shifted towards exploiting DLP and TLP with multicore designs increasing multi-threaded performance
Now, it’s pretty clear that even exploiting TLP has reached its limits and we’ve entered the age of specialization
Some examples from three of the biggest companies in industry show tight coupling between general-purpose cores with specialized accelerators (mostly graphics)

## Slide 3: Motivation
Heterogeneous architectures introduce host of concerns:
  Common programming framework
  Compiler/runtime support
  Scheduling work optimally (performance? utilization? energy?)
  Heuristics for adaptive execution
  How to expose parallelism that can be commonly exploited?
Motivation Data Parallelism XPC Hardware XPC Software Adaptive Acceleration
3/21

## Slide 4: Traditional Data Parallelism
Motivation Data Parallelism XPC Hardware XPC Software Adaptive Acceleration
4/21
vvadd( int* dest, int* src0, int* src1, int size ):
for i in range( size ):
dest[i] = src0[i] + src1[i]
Notes: Same task operates on independent pieces of data (elements)
Note that both the control flow and data structure are highly regular
Each task operates on an element of each of the source arrays and produces an element of the output array (the inputs and outputs are disjoint)

## Slide 5: Amorphous Data Parallelism
Motivation Data Parallelism XPC Hardware XPC Software Adaptive Acceleration
5/21
bfs( Node* nodes, Worklist* wl ):
while wl not empty:
index = wl->pull()
my_node = node[index]
for all neighbors of my_node:
if my_node.dist + 1 < neighbor.dist:
neighbor.dist = my_node.dist + 1
wl->push( neighbor.index )
Notes: Different from vvadd, elements of tasks can overlap, requiring some conflict resolution
Another key difference is that we are dynamically generating tasks as we traverse the graph, instead of having all tasks available before we start computation

## Slide 6: Traditional vs. Amorphous Data Parallelism
Motivation Data Parallelism XPC Hardware XPC Software Adaptive Acceleration
6/21
Characteristic | Traditional | Amorphous
Control Flow | Regular | Irregular
Data Structure | Regular | Irregular
Task Inputs/Outputs | Disjoint | Overlapped
Task Generation | Static | Dynamic
Notes: * Intuition is that if we can capture amorphous data parallelism, could we ubiquitously exploit this parallelism on any workload?
----- Meeting Notes (9/19/14 11:15) -----
* Data-dependent execution

## Slide 7: Objective
Explicit Parallel Call (XPC) architecture composed of microarchitectural tiles capable of exploiting varying degrees of amorphous data parallelism exposed as parallel function calls
Motivation Data Parallelism XPC Hardware XPC Software Adaptive Acceleration
7/21
Notes: XPC programming API for more algorithm-centric approach to writing applications
XPC runtime which facilitates adaptive task scheduling and migration

## Slide 8: Pull-Based Parallelism
Motivation Data Parallelism XPC Hardware XPC Software Adaptive Acceleration
8/21
 | Software | Hardware
Expressing opportunities for parallel tasks | Parallel function calls (tasks stored in memory) | Special memory instructions for updating tasks
Stealing parallel tasks | Adaptive runtime | Task cache
Executing parallel tasks | Application running on native multicore | Amorphous data parallel accelerators
XPC as a point in the design space of pull-based parallelism
Use hardware to accelerate some or all facets
Notes: * Pull model where functions may or may not be executed in parallel, as opposed to push model we are more used to like bthreads where we actively push tasks onto threads

## Slide 9: XPC Hardware: ISA
Motivation Data Parallelism XPC Hardware XPC Software Adaptive Acceleration
9/21
Instruction | Description
pcall n, func | Make n instances of function available for parallel execution (serial execution is valid)
psync | Wait for all child parallel calls to complete
pret | Return from parallel call (uses different return address from standard function call)
Notes: * Pull model where functions may or may not be executed in parallel, as opposed to push model we are more used to like bthreads where we actively push tasks onto threads

## Slide 10: XPC Hardware: Tightly-Coupled Lanes (TCL)
Motivation Data Parallelism XPC Hardware XPC Software Adaptive Acceleration
10/21
High performance and energy efficiency for traditional data parallelism
Amortized front-end, lock-step execution
Affine execution accelerates value structure
Suffers with control and memory-access irregularity
Notes: * Unclear how to exploit nested parallelism (traditional execution)?

## Slide 11: XPC Hardware: Loosely-Coupled Lanes (LCL)
Motivation Data Parallelism XPC Hardware XPC Software Adaptive Acceleration
11/21
Better tolerance for irregular amorphous data parallelism
Decoupled control flow between lanes using instruction buffers
More lightweight lanes with shared ‘expensive’ FUs
Good middle-ground specialization before resorting to general-purpose
Notes: Dynamic bound, communicate back to lane manager?
Still depends on some level of regularity and control flow divergence constrained by size of instruction buffer

## Slide 12: XPC Hardware: Cooperative Multicore (CMC)
Motivation Data Parallelism XPC Hardware XPC Software Adaptive Acceleration
12/21
General-purpose, capable of handling highly irregular amorphous data parallelism
No significant performance or energy benefits regular control and memory-access
Internal task distribution unit
Default tile to collect heuristics for migration?

## Slide 13: XPC Software: Programming API
13/21
Highly productive parallel programming API
  Subset of PARC Parallel Primitives (PPP)
Algorithm-centric approach with a focus on exposing amorphous data parallelism
Four parallel constructs
  spawn
  parallel_for
  atomic_for
  speculative_for
Motivation Data Parallelism XPC Hardware XPC Software Adaptive Acceleration

## Slide 14: XPC Software: Programming API
14/21
spawn( index, function )
  Recursive divide-and-conquer
void bfs( Node* nodes ) {
ppp<xpc>::spawn( start, func = [&] ( int idx ) {
Node my_node = node[idx];
for ( i = 0; i < my_node.num_neighbors; i++ ) {
Node neighbor = my_node.neighbors[idx];
if ( my_node.dist + 1 < neighbor.dist ) {
neighbor.dist = my_node.dist + 1;
xpc::spawn( neighbor.idx, func );
}
}
});
}
Motivation Data Parallelism XPC Hardware XPC Software Adaptive Acceleration

## Slide 15: XPC Software: Programming API
15/21
parallel_for( num_calls, function )
  Parallelize across loop iterations (i.e., tasks)
void bfs( Node* nodes ) {
Worklist inwl, outwl;
inwl.push( start );
while ( inwl.size() > 0 ) {
ppp<xpc>::parallel_for( inwl.size(), [&] ( int idx ) {
Node my_node = node[inwl.pull(idx)];
for ( i = 0; i < my_node.num_neighbors; i++ ) {
Node neighbor = my_node.neighbors[i];
if ( my_node.dist + 1 < neighbor.dist ) {
neighbor.dist = my_node.dist + 1;
outwl.push( neighbor.idx );
}
}
});
swap( inwl, outwl );
}
}
Motivation Data Parallelism XPC Hardware XPC Software Adaptive Acceleration

## Slide 16: XPC Software: Programming API
16/21
atomic_for( num_calls, function )
  Similar to parallel_for except tasks are guaranteed atomicity
void mm( Edge* out_edges, Edge* in_edges ) {
bool matched[num_nodes];
ppp<xpc>::atomic_for( num_edges, [&] ( int idx ) {
int u = in_edges[idx].u;
int v = in_edges[idx].v;
if ( !matched[u] && !matched[v] ) {
matched[u] = matched[v] = true;
out_edges[idx] = in_edges[idx];
}
});
}
Motivation Data Parallelism XPC Hardware XPC Software Adaptive Acceleration
Notes: Fine subset of edges which span all nodes exactly once

## Slide 17: XPC Software: Programming API
17/21
speculative_for( num_calls, reserve_func, commit_func )
  Split tasks into reserve and commit phases to ensure atomicity
void mm( Edge* out_edges, Edge* in_edges ) {
ppp<xpc>::speculative_for( num_edges,
reserve_func = [&] ( int idx ) {
int u = in_edges[idx].u;
int v = in_edges[idx].v;
if ( matched[u] || matched[v] ) return false;
reserves[u] = reserves[v] = idx;
return true;
},
commit_func = [&] ( int idx ) {
if ( reserves[u] == reserves[v] == idx ) {
matched[u] = matched[v] = true;
out_edges[idx] = in_edges[idx];
return true;
}
return false;
}
);
}
Motivation Data Parallelism XPC Hardware XPC Software Adaptive Acceleration

## Slide 18: XPC Software: Adaptive Runtime
Motivation Data Parallelism XPC Hardware XPC Software Adaptive Acceleration
18/21
Software-based adaptive execution
  Always running on idle tiles to facilitate work stealing
  Ideal if lightweight to minimize software overhead
Collect heuristics to determine when/where to schedule tasks
  Raw performance (compare to threshold or history)
  Control irregularity (e.g., number of warp fragments)
  Memory-access irregularity (e.g., number of uncoalesced accesses)
Hardware support for runtime?
  Inter-tile task distribution unit exposed to runtime (not to user)
  Hardware performance counters for heuristics

## Slide 19: Adaptive Acceleration
Motivation Data Parallelism XPC Hardware XPC Software Adaptive Acceleration
19/21
Reasonable design point for exploring XPC
Single tile with three sub-tiles: scalar CP, TCL, LCL
CP responsible for generating work which can be stolen by TCL or LCL accelerators
Shared memory system minimizes migration overhead

## Slide 20: Adaptive Acceleration
Motivation Data Parallelism XPC Hardware XPC Software Adaptive Acceleration
20/21
Design decision challenges
  Role of CP: completely independent of accelerators? TCL/LCL requires separate front-end (e.g., internal CP?)
  Degree of HW support: focusing on single-tile makes HW migration more viable vs. SW runtime, but requires finite-capacity buffer?
  Mapping parallel functions: if preferred accelerator is not available, still run it on any available sub-tile (including CP)?

## Slide 21: Adaptive Acceleration
Motivation Data Parallelism XPC Hardware XPC Software Adaptive Acceleration
21/21
Nested parallelism
  Interesting opportunities to more generically expose previously underutilized parallelism!
  Allow any level of nesting to produce generic fine-grain tasks that can map to any sub-tile (function pointer, context pointer, call count)
  Hardware support for nested parallelism on TCL? (LCL can handle)
    pcall instruction on TCL triggers push to special task buffer which lazily updates memory? Would not look like function call in TCL, no divergence